## Slide 1
Embedded Systems
INSA Summer Camp
STM32 Low-Power Modes and Wake-Up Mechanisms
By: Nebiyat Biadglign
September 2026
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
1 / 19

## Slide 2
STM32F103C8T6 — Device Overview
ARM Cortex-M3 Medium-Density Performance Line
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
2 / 19
Source: DS5319 Rev. 20, July 2025
Core Specifications
CPU Core
ARM Cortex-M3 (ARMv7-M architecture)
Max Frequency
72 MHz
Flash Memory
64 KB (C8 variant — C8 ≠ CB which has 128 KB)
SRAM
20 KB
Supply Voltage
2.0 V – 3.6 V (VDD) | 2.0 – 3.6 V (VDDA)
Package
LQFP48 | UFQFPN48
Temp. Range
–40°C to +85°C (TA)
GPIO
37 I/O pins (LQFP48), 4-bit mode/CNF per pin
ADC
2× 12-bit SAR ADC, 10 external channels
Timers
TIM1 (advanced), TIM2/3/4 (general-purpose)
Comms
3× USART, 2× SPI, 2× I²C
USB / CAN
USB 2.0 Full-Speed | bxCAN 2.0B
DMA
7-channel DMA controller (AHB master)
Key Device Distinctions
Family context
STM32F103 is the medium-density performance line. The family covers 64 KB (C8) and 128 KB (CB) Flash variants. This presentation covers the C8 (64 KB).
Cortex-M3 core
32-bit RISC, Thumb-2 ISA, single-cycle multiply, hardware divide. No floating-point unit. NVIC with 68 maskable interrupt lines.
Official low-power modes
Sleep — Stop — Standby
Shutdown mode — NOT supported by STM32F103C8T6
Shutdown belongs to newer STM32L/STM32G families and must not be presented as an F103 feature.
Bus architecture & frequencies
AHB bus (up to 72 MHz max): core, DMA, Flash, SRAM. APB2 (up to 72 MHz max): GPIO, ADC, TIM1, USART1, SPI1. APB1 (up to 36 MHz max): TIM2–4, USART2/3, SPI2, I²C, USB, CAN.

## Slide 3
ARM Cortex-M3 Architecture
ARMv7-M | NVIC | SysTick | SCB | WFI / WFE
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
3 / 19
Source: DS5319 Rev. 20; RM0008 Rev. 21; ARM DDI 0337
Core Features
• ARM Cortex-M3 (ARMv7-M profile)
• Thumb-2 instruction set — 16/32-bit mixed encoding
• 3-stage pipeline, single-cycle multiply, hardware divide
• No FPU (floating-point unit not present in M3)
•
• NVIC — Nested Vectored Interrupt Controller
• 68 maskable interrupt sources
• 16 priority levels (4-bit priority field)
• Tail-chaining and late-arrival optimisation
•
• SysTick — 24-bit countdown timer
• Provides OS tick; can wake from Sleep mode
•
• System Control Block (SCB)
• SCB→SCR controls sleep-entry behaviour
• SLEEPDEEP bit selects Sleep vs Stop/Standby
• SLEEPONEXIT: re-enter sleep after ISR returns
• SEVONPEND: pending IRQ generates wake event
WFI — Wait For Interrupt
• CPU halts and waits for a pending enabled interrupt
• Interrupt fires → CPU wakes, ISR executes
• Most common mechanism for interrupt-driven sleep
• Used in Sleep, Stop, and Standby modes
• CMSIS: __WFI() or __asm("WFI")
WFE — Wait For Event
• CPU halts and waits for an event signal
• Event does not require ISR entry — processor simply resumes
• Event sources: SEV instruction, EXTI event, SEVONPEND
• Used for event-driven synchronisation / low-power loops
• CMSIS: __WFE() | __SEV() before WFE if latch is empty
SCB→SCR Key Bits
SLEEPDEEP [2]
0 = Sleep on WFI/WFE | 1 = Stop or Standby on WFI/WFE
SLEEPONEXIT [1]
Re-enter sleep mode automatically after ISR completes
SEVONPEND [4]
Pending interrupt (even masked) acts as wake event for WFE

## Slide 4
Memory, Bus and Peripheral Architecture
AHB / APB1 / APB2 | DMA | Peripheral Overview
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
4 / 19
Source: DS5319 Rev. 20, Fig. 1, p. 11
Core & Memory (AHB — up to 72 MHz)
Flash
64 KB, 128-bit bus, zero-wait (at ≤24 MHz)
SRAM
20 KB, single-cycle access, retained in Stop
DMA
7-ch AHB master, mem-to-mem & periph modes
NVIC
68 IRQs, 16 priority levels, vector table
SysTick
24-bit, 1 ms OS tick, wake from Sleep
Debug
SW-DP / JTAG, TPIU trace interface
Boot ROM
Factory bootloader (USART1/USB DFU)
BKP
10× 16-bit backup data registers (VBAT)
APB1 Peripherals (max 36 MHz)
TIM2–4
General-purpose, 4 channels each
USART2–3
Async / sync serial, SmartCard, IrDA
SPI2
Full-duplex, up to 18 Mbps
I²C 1–2
Standard / Fast mode, SMBus
bxCAN
CAN 2.0B, 3 TX + 2 RX mailboxes
USB
2.0 FS, 512 B SRAM, no ext. PHY needed
PWR
Power control registers (CR, CSR)
BKP ctrl
Backup domain control + tamper
APB2 Peripherals (max 72 MHz)
TIM1
Advanced motor-control, complementary out
GPIOA–E
37 I/O, CRL/CRH (4 bits/pin)
USART1
High-speed async, up to 4.5 Mbps
SPI1
High-speed, up to 18 Mbps
ADC1–2
12-bit SAR, dual mode, 10 ext. channels
AFIO
Alternate function remap + EXTI routing
EXTI
16 GPIO + 4 internal interrupt/event lines
RCC
Clock generation, prescalers, reset control

## Slide 5
Clock and Reset System (RCC)
HSI / HSE / PLL / LSI / LSE | Derived Clocks | Clock Gating
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
5 / 19
Source: DS5319 Rev. 20, Fig. 2, p. 12; RM0008 Rev. 21, §7
Clock Sources
HSI — High-Speed Internal (8 MHz)
RC oscillator, factory-calibrated. Selected by default after reset. Fast start-up (~8 cycles). Can drive PLL as HSI/2 (4 MHz source).
HSE — High-Speed External (4–16 MHz)
External crystal or oscillator. Enables PLL to reach 72 MHz. CSS (Clock Security System) monitors HSE and can fall back to HSI.
PLL — Phase-Locked Loop (up to 72 MHz)
Source: HSI/2 or HSE. PLLMUL × 2…16. SYSCLK = PLL output. Must be ≤72 MHz.
LSI — Low-Speed Internal (~40 kHz)
RC oscillator; feeds IWDG. Optional RTC clock source. Active in Stop and Standby if IWDG is running.
LSE — Low-Speed External (32.768 kHz)
Crystal oscillator in VBAT domain. Primary RTC clock source. Retained in Stop and Standby modes.
Derived Clocks
SYSCLK
System clock — HSI, HSE, or PLL output (≤72 MHz)
HCLK
AHB clock = SYSCLK / AHB prescaler (core, DMA, SRAM)
PCLK1
APB1 clock = HCLK / APB1 prescaler (≤36 MHz)
PCLK2
APB2 clock = HCLK / APB2 prescaler (≤72 MHz)
ADCCLK
PCLK2 / 2/4/6/8 (≤14 MHz for 12-bit conversion)
RTCCLK
LSE (preferred) or LSI or HSE/128
IWDGCLK
LSI only — independent watchdog always uses LSI
Clock Gating — Power Relevance
• Each APB1/APB2 peripheral has a dedicated clock-enable bit:
• RCC_APB1ENR and RCC_APB2ENR
• Disabling unused peripherals before WFI reduces dynamic current
• in Run mode and maximises power savings in Sleep mode.
•
• In Stop mode, all APB/AHB clocks are halted automatically
• regardless of the RCC enable bits.

## Slide 6
GPIO, NVIC and EXTI
External Interrupt/Event Lines | Wake-Up Path
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
6 / 19
Source: RM0008 Rev. 21, §9 (GPIO), §10 (EXTI), §4.3 (NVIC)
GPIO
• 37 I/O pins available on LQFP48 package
• Ports PA through PE (up to 16 pins each)
• Configured per-pin via GPIOx_CRL (pins 0–7)
• and GPIOx_CRH (pins 8–15)
•
• 4 bits per pin: MODE[1:0] + CNF[1:0]
• MODE=00: Input mode
• MODE=01/10/11: Output at 2/10/50 MHz
•
• Pull-up / Pull-down (input mode):
• CNF=10b enables pull; ODR=1 → pull-up
• ODR=0 → pull-down
•
• GPIO as wake-up source:
• Route through AFIO_EXTICRx to EXTI line
• then configure EXTI + NVIC for interrupt
EXTI — External Interrupt/Event
• 19 EXTI lines in STM32F103 (EXTI0–EXTI18):
• Lines 0–15: configurable from any GPIO pin (PA–PE)
• Line 16: connected to PVD output
• Line 17: connected to RTC Alarm event
• Line 18: connected to USB Wakeup event
• (Line 19 is Ethernet in connectivity line F105/107 only)
•
• Configuration registers:
• EXTI_IMR — Interrupt mask (unmask = enable IRQ)
• EXTI_EMR — Event mask (unmask = enable event)
• EXTI_RTSR — Rising trigger select register
• EXTI_FTSR — Falling trigger select register
• EXTI_PR — Pending register (clear by writing 1)
•
• Interrupt path: EXTI → NVIC → CPU ISR
• Event path: EXTI → WFE wake (no ISR needed)
Interrupt Wake-Up Flow
GPIO pin (PA0–PE15)
▼
AFIO_EXTICRx (port → EXTI line)
▼
EXTI_RTSR / FTSR (edge selection)
▼
EXTI_IMR bit set (unmask interrupt)
▼
NVIC_ISER bit set (enable IRQ)
▼
Execute WFI (CPU sleeps)
▼
Edge detected → EXTI_PR set
▼
NVIC activates IRQ
▼
ISR executes (CPU awake)

## Slide 7
STM32F103C8T6 Power-Control Architecture
VDD Domains | Internal Regulator | PWR | RCC | Cortex-M3 SCB
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
7 / 19
Source: RM0008 Rev. 21, §5 (PWR); §7 (RCC)
Power Domains
VDD (2.0–3.6 V)
Main supply — I/O pads & 1.8V regulator. Externally supplied in all operational modes.
VDDA (2.0–3.6 V)
Analog supply — ADC, reset, RC, PLL. Must be at same potential as VDD (VDDA = VDD).
1.8 V Core Domain
Supplied by internal regulator from VDD. Powers CPU core, SRAM, and digital logic. ON in Run/Sleep/Stop; powered off in Standby.
VBAT (1.65–3.6 V)
Backup domain — RTC, BKP regs, LSE (32 kHz). Powered via VBAT pin when VDD is off. Active in ALL modes incl. Standby.
Low-Power Control Hierarchy
Cortex-M3 Core
SCB→SCR: SLEEPDEEP bit WFI / WFE instructions
↓
PWR Peripheral
PWR_CR: PDDS, LPDS, DBP PWR_CSR: EWUP, WUF, SBF
↓
RCC Controller
Clock enable/disable HSI/HSE/PLL on-off control
↓
EXTI Controller
Interrupt & Event routing Wake-up trigger selection
↓
NVIC
IRQ enable, priority Pending / active tracking
Low-Power Entry Sequence
1. Configure EXTI / NVIC (select wake-up source)
▼
2. SCB→SCR.SLEEPDEEP (0 = Sleep; 1 = Stop/Standby)
▼
3. PWR_CR: PDDS + LPDS (mode and regulator select)
▼
4. Write PWR_CR.CWUF = 1 (clear stale wake-up flag)
▼
5. Execute WFI or WFE (processor halts)
▼
6. Wake-up event/interrupt (clocks restore, resume code)

## Slide 8
STM32F103C8T6 — Low-Power Modes
Official modes per RM0008 Rev. 21, §5.3 | Sleep | Stop | Standby
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
8 / 19
Source: RM0008 Rev. 21, §5.3, Table 11, p. 72
SLEEP
SLEEPDEEP
= 0 (SCB→SCR)
PDDS
N/A
CPU
Halted (WFI or WFE)
Peripherals
All clocks continue
SRAM
Retained ✓
Regulator
ON — normal
Wake sources
Any enabled interrupt / event
Restart
Resumes from next instruction
Typical use
Short idle between tasks
STOP
SLEEPDEEP
= 1 (SCB→SCR)
PDDS
= 0 (PWR_CR)
CPU
Halted (WFI or WFE)
All clocks
HSI, HSE, PLL stopped
SRAM
Retained ✓
Regulator
ON or low-power (LPDS bit)
Wake sources
EXTI lines, RTC, NRST
After wake
HSI selected — restore PLL if needed
Typical use
Extended idle, sensor nodes
STANDBY
SLEEPDEEP
= 1 (SCB→SCR)
PDDS
= 1 (PWR_CR)
CPU
Halted (WFI or WFE)
1.8V domain
POWERED DOWN
SRAM
CONTENTS LOST ✗
Regulator
OFF
Wake sources
WKUP pin, RTC, NRST, IWDG
After wake
Reset-like restart — reinitialise all
Typical use
Maximum saving, RTC periodic wake

## Slide 9
Sleep Mode
SLEEPDEEP = 0 | WFI / WFE | Low-Power Sleep Clarification
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
9 / 19
Source: RM0008 Rev. 21, §5.3.1
Sleep Mode Configuration
Entry condition:
WFI or WFE executed with SCB→SCR.SLEEPDEEP = 0
What remains ON:
CPU core: halted — saves active power
SRAM: retained (all contents safe)
Peripheral clocks: all continue (SYSCLK, HCLK, PCLK1, PCLK2)
DMA, USART, Timers, ADC: continue operating
Voltage regulator: ON, normal mode
Wake-up sources:
Any enabled NVIC interrupt (EXTI, timer, DMA, USART, ADC…)
Any event configured in EXTI_EMR (for WFE path)
SysTick, RTC alarm, peripheral events
Power reduction:
Lower than Run mode — CPU core halted
Higher than Stop mode — clocks still active
Low-Power Sleep
What RM0008 Rev. 21 actually defines:
RM0008 does not define a separate 'Low-Power Sleep Mode' for STM32F103C8T6. The three official modes are Sleep, Stop, and Standby.
The LPDS bit (Low-Power in Deepsleep):
LPDS is bit 0 of PWR_CR. It controls the internal voltage regulator behaviour during Stop mode — not a sub-mode of Sleep. LPDS = 1 puts the regulator into low-power mode when in Stop, reducing quiescent current at the cost of slightly longer wake-up latency.
Correct interpretation of 'Low-Power Sleep':
• Gating unused APB peripheral clocks (RCC_APB1ENR / APB2ENR)
• Reducing SYSCLK frequency before entering Sleep
• Using SLEEPONEXIT to stay in sleep after each ISR
• Disabling the ADC and other power-hungry blocks when idle
.

## Slide 10
Stop Mode
SLEEPDEEP = 1, PDDS = 0 | All Clocks Off | SRAM Retained
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
10 / 19
Source: RM0008 Rev. 21, §5.3.2
Stop Mode Configuration
Entry registers:
SCB→SCR.SLEEPDEEP = 1
PWR_CR.PDDS = 0 (Stop, not Standby)
PWR_CR.LPDS = 0 or 1 (regulator normal or low-power)
Then execute: WFI or WFE
What happens:
HSI oscillator: STOPPED
HSE oscillator: STOPPED
PLL: STOPPED
All 1.8V domain clocks: STOPPED
SRAM contents: RETAINED ✓
Register contents: RETAINED ✓
Voltage regulator: ON (normal or low-power via LPDS)
LSE / LSI: continue if enabled (RTC domain)
Wake-up sources:
Any EXTI line configured in EXTI_IMR + NVIC
RTC alarm (EXTI line 17) / RTC wake-up timer
NRST pin (external reset — causes full reset)
LPDS = 1 note:
Lower regulator quiescent current; wake-up latency slightly longer.
Stop Mode — Entry / Exit Sequence
Normal operation (HSE+PLL, 72 MHz)
▼
Gate unused peripheral clocks
▼
Configure EXTI wake-up source
▼
SCB→SCR: SLEEPDEEP = 1
▼
PWR_CR: PDDS = 0 (+ optional LPDS)
▼
Clear PWR_CR.CWUF (wake-up flag)
▼
Execute WFI or WFE
▼
— All 1.8V domain clocks halt —
▼
Wake-up event occurs
▼
HSI auto-selected as SYSCLK (8 MHz)
▼
Restore HSE + PLL if 72 MHz needed
▼
Resume application code
Critical: Clock Restore After Stop Wake-Up
After Stop wake-up, the system clock source automatically defaults to HSI (8 MHz). If the application requires HSE and PLL for full 72 MHz operation, firmware must: re-enable HSE → wait for HSERDY → re-enable PLL → wait for PLLRDY → switch SYSCLK to PLL. This must be coded explicitly in the wake-up path.

## Slide 11
Standby Mode
SLEEPDEEP = 1, PDDS = 1 | 1.8V Domain Powered Down | SRAM Lost
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
11 / 19
Source: RM0008 Rev. 21, §5.3.3
Standby Mode Configuration
Entry registers:
SCB→SCR.SLEEPDEEP = 1
PWR_CR.PDDS = 1 (Standby, not Stop)
Then execute: WFI or WFE
What happens:
1.8V core domain: POWERED DOWN
SRAM: CONTENTS LOST ✗
CPU registers: LOST
HSI, HSE, PLL: STOPPED
Voltage regulator: OFF
Backup domain (VBAT): RETAINED ✓
RTC (if running from LSE/LSI): RETAINED ✓
Backup registers (BKP1R–BKP10R): RETAINED ✓
Wake-up sources (limited):
WKUP pin (PA0, rising edge) — requires PWR_CSR.EWUP = 1
RTC alarm event (EXTI line 17)
External reset on NRST pin
IWDG reset (if IWDG was running)
Wake-up behaviour:
Behaves like a power-on reset. All peripherals and SRAM must be fully reinitialised. PWR_CSR.SBF flag indicates Standby was the previous state.
Stop vs Standby Comparison
Feature | Stop Mode | Standby Mode
PDDS bit | = 0 | = 1
1.8V core domain | ON | OFF
SRAM | Retained ✓ | LOST ✗
Registers | Retained ✓ | LOST ✗
Backup (VBAT) | Retained ✓ | Retained ✓
RTC | Runs (VBAT domain) | Runs (VBAT domain)
Regulator | ON / low-pwr (LPDS) | OFF
EXTI wake-up | Yes ✓ | No (limited sources)
WKUP pin (PA0) | Yes ✓ | Yes (EWUP=1 required)
RTC alarm wake | Yes ✓ | Yes ✓
NRST wake | Yes ✓ | Yes ✓
IWDG reset | Yes ✓ | Yes ✓
After wake | Code resumes (HSI) | Reset-like restart
Power reduction | Very low (SRAM kept) | Lowest (1.8V off)

## Slide 12
Low-Power Mode Comparison
Sleep | Stop | Standby | RM0008 Rev. 21, Table 11, p. 72
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
12 / 19
Source: RM0008 Rev. 21, §5.3, Table 11, p. 72
Official RM0008 Table 11 — Low-Power Mode Summary:
Feature | Sleep | Stop | Standby
Entry instruction | WFI or WFE | WFI or WFE | WFI or WFE
SLEEPDEEP bit | = 0 | = 1 | = 1
PDDS bit (PWR_CR) | N/A | = 0 | = 1
CPU core | Halted | Halted | Halted
Peripheral clocks | All running | All stopped | All stopped
HSI / HSE / PLL | Running | Stopped | Stopped
SRAM | Retained ✓ | Retained ✓ | LOST ✗
Registers | Retained ✓ | Retained ✓ | LOST ✗
Voltage regulator | ON — normal | ON or low-power (LPDS) | OFF
Backup domain (VBAT) | Retained | Retained | Retained
RTC / LSE | Runs if enabled | Runs (VBAT domain) | Runs (VBAT domain)
Wake-up sources | Any IRQ / Event | EXTI, RTC, NRST | WKUP, RTC, NRST, IWDG
After wake-up | Resumes from WFI | Resumes (HSI default) | Reset-like restart
Power consumption | Low (CPU halted) | Very low (clocks off) | Lowest consumption
Typical use | Short idle periods | Extended idle, sensors | Max saving, RTC wake

## Slide 13
Low-Power Control Registers
PWR | RCC | SCB | EXTI | NVIC
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
13 / 19
Source: RM0008 Rev. 21, §5.4 (PWR), §7 (RCC), §10 (EXTI)
Power Control (PWR)
PWR_CR
Power control — PDDS, LPDS, CWUF, CSBF, PVDE, DBP
PWR_CSR
Status/ctrl — EWUP (WKUP), WUF, SBF, PVDO
RCC_CR
Clock ctrl — HSION, HSEON, PLLON, HSIRDY, HSERDY
RCC_CFGR
Clock config — SW[1:0], SWS, HPRE, PPRE1/2, PLLSRC/MUL
RCC_APB1ENR
APB1 clock enables — TIM2–4, USART2/3, SPI2, I2C, USB, CAN
RCC_APB2ENR
APB2 clock enables — GPIOA–E, USART1, SPI1, ADC1/2, TIM1
RCC_BDCR
Backup domain — LSEON, LSERDY, RTCSEL, RTCEN
RCC_CSR
Status — LSION, LSIRDY, reset source flags (PORRSTF…)
Cortex-M3 SCB + EXTI
SCB→SCR
Sleep ctrl — SLEEPDEEP, SLEEPONEXIT, SEVONPEND
SCB→ICSR
Pending/active IRQ state, NMI/SysTick pending bits
EXTI_IMR
Interrupt mask — bit n=1 enables IRQ on line n
EXTI_EMR
Event mask — bit n=1 enables event on line n
EXTI_RTSR
Rising trigger select — rising edge on EXTI line n
EXTI_FTSR
Falling trigger select — falling edge on EXTI line n
EXTI_SWIER
Software trigger — force EXTI event via software
EXTI_PR
Pending register — clear by writing 1 to bit n
NVIC + AFIO
NVIC_ISER
Set-enable — write 1 to bit n to enable IRQ n in NVIC
NVIC_ICER
Clear-enable — write 1 to bit n to disable IRQ n
NVIC_ISPR
Set-pending — force IRQ n into pending state
NVIC_ICPR
Clear-pending — remove IRQ n from pending state
NVIC_IABR
Active-bit register — read-only, which IRQs are active
NVIC_IPRn
Priority — 4-bit field per IRQ (bits [7:4], 0=highest, 15=lowest)
AFIO_EXTIR
EXTI source select — 4 bits/line (chooses GPIO port for EXTI 0–15)
SCB→VTOR
Vector table offset — IRQ handler base address

## Slide 14
Important Register Bits
PWR_CR | PWR_CSR | SCB→SCR | EXTI
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
14 / 19
PWR_CR — Power Control Register
Bit | Name | Function
Bit 0 | LPDS | Regulator low-power in Deepsleep: 1 = low-power mode in Stop
Bit 1 | PDDS | Power-down Deepsleep: 0 = Stop mode; 1 = Standby mode on WFI/WFE
Bit 2 | CWUF | Clear wake-up flag: write 1 to clear WUF bit in PWR_CSR
Bit 3 | CSBF | Clear standby flag: write 1 to clear SBF bit in PWR_CSR
Bit 4 | PVDE | Programmable voltage detector enable
Bit 7:5 | PLS | PVD level: 000=2.2V, 001=2.3V … 111=2.9V threshold
Bit 8 | DBP | Disable backup write protection: 1 = enables write to RTC & BKP
PWR_CSR — Power Control/Status Register
Bit | Name | Function
Bit 0 | WUF | Wake-up flag: set when WKUP pin is high or RTC event occurs
Bit 1 | SBF | Standby flag: set when device was previously in Standby mode
Bit 2 | PVDO | PVD output: 1 = VDD is below the selected PVD threshold
Bit 8 | EWUP | Enable WKUP pin PA0 as Standby wake-up source
SCB→SCR and EXTI Key Bits
Register | Bit / Field | Function
SCB→SCR | SLEEPDEEP [2] | 0 = Sleep on WFI; 1 = Stop or Standby on WFI
SCB→SCR | SLEEPONEXIT [1] | Sleep on return from ISR (stay in sleep loop)
SCB→SCR | SEVONPEND [4] | Pending IRQ (even if masked) acts as WFE event
EXTI_IMR | MR[n] | 1 = interrupt from EXTI line n is unmasked
EXTI_EMR | MR[n] | 1 = event from EXTI line n is unmasked (for WFE)
EXTI_RTSR | TR[n] | 1 = rising edge on EXTI line n triggers event/IRQ
EXTI_FTSR | TR[n] | 1 = falling edge on EXTI line n triggers event/IRQ
EXTI_PR | PR[n] | Pending flag for line n; clear by writing 1
NVIC_ISER | SETENA[n] | Write 1 to bit n to enable IRQ n in the NVIC
NVIC_IPRn | IP[n] [7:4] | 4-bit priority for IRQ n (0 = highest; 15 = lowest)

## Slide 15
WFI vs WFE — Wait For Interrupt / Event
ARM Cortex-M3 Sleep-Entry Instructions
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
15 / 19
Source: ARM DDI 0337; RM0008 Rev. 21, §5.3
WFI — Wait For Interrupt
Mechanism:
The CPU halts and enters a low-power state. Execution resumes when a pending interrupt is present and is enabled in the NVIC.
Configuration steps:
1. Configure the interrupt source (e.g. EXTI, TIM, USART)
2. Enable the IRQ in NVIC_ISER
3. Execute __WFI() (or __asm("WFI"))
4. Interrupt fires → CPU wakes and ISR executes
Key properties:
Interrupt-driven — ISR always runs on wake-up
Works in Sleep, Stop, and Standby modes
PRIMASK = 1 can prevent ISR but wake still occurs
FAULTMASK blocks all exceptions except NMI and reset
Most common mechanism for low-power embedded systems
CMSIS intrinsic:
__WFI();
WFE — Wait For Event
Mechanism (ARMv7-M Architecture):
The CPU checks its internal single-bit Event Register. If the Event Register is set (1), WFE clears it to 0 and executes immediately without sleeping. If the Event Register is 0, WFE suspends CPU execution until an event occurs.
Event sources:
SEV instruction executed by processor or debug subsystem
EXTI line configured as event mode in EXTI_EMR (not EXTI_IMR)
Any enabled NVIC interrupt when SCB→SCR.SEVONPEND = 1
Key distinctions from WFI:
Event wake-up does NOT require an ISR to execute (processor resumes directly)
Eliminates interrupt stacking/unstacking latency (zero ISR overhead)
If woken by EXTI event (EMR unmasked, IMR masked), no ISR is called
If woken with PRIMASK = 1, WFE resumes without taking interrupt handlers
Widely used in low-latency event polling and RTOS idle loops
CMSIS intrinsic:
__WFE(); // Wait For Event
// Recommended pattern to clear pre-existing event latch before sleep:
__SEV(); __WFE(); __WFE();

## Slide 16
Interrupt and Wake-Up Mechanisms
EXTI | GPIO Events | RTC | WKUP Pin | NRST | IWDG
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
16 / 19
Source: RM0008 Rev. 21, §5.3, §10 (EXTI), §18 (RTC)
IRQ Wake-Up Path (WFI)
GPIO Pin (PAx–PEx)
▼
AFIO_EXTICRx (port→line)
▼
EXTI_RTSR/FTSR (edge)
▼
EXTI_IMR (unmask IRQ)
▼
NVIC_ISER (enable)
▼
CPU: WFI → edge detected
▼
EXTI pending → NVIC → ISR
Event Wake-Up Path (WFE)
Event source (EXTI / SEV)
▼
EXTI_EMR (unmask event)
▼
CPU: WFE (sleeping)
▼
Event signal arrives
▼
Event latch cleared
▼
CPU resumes (no ISR required)
Sources by Mode
Source | Sleep | Stop | Standby
Any IRQ | ✓ | EXTI only | ✗
EXTI GPIO | ✓ | ✓ | ✗
RTC alarm | ✓ | ✓ | ✓
WKUP (PA0) | ✓ | ✓ | ✓ (EWUP=1)
NRST | ✓ | ✓ | ✓ (reset)
IWDG reset | ✓ | ✓ | ✓ (reset)
Timers | ✓ | ✗ | ✗
Wake-Up Source Details
External Interrupts (EXTI 0–15)
16 GPIO-mapped lines. Rising/falling/both edge. Configured via AFIO_EXTICRx, EXTI_RTSR/FTSR, EXTI_IMR, NVIC_ISER. Valid in Sleep and Stop mode.
GPIO Events (EXTI_EMR)
Same EXTI hardware routed via EXTI_EMR. Wakes CPU from WFE without triggering an ISR. Edge detection and trigger selection same as interrupt path.
RTC Alarm / Wake-Up Timer
RTC in VBAT domain, clocked by LSE (32.768 kHz). Alarm triggers EXTI line 17. Valid in Sleep, Stop, and Standby. Must be configured before entering low-power mode.
WKUP Pin (PA0)
Dedicated Standby wake-up pin. Requires PWR_CSR.EWUP = 1. Rising edge on PA0 sets WUF flag and wakes from Standby. Also works in Sleep/Stop as a normal EXTI.
NRST (External Reset)
Always active in all modes. Pulling NRST low initiates a full system reset. Not a clean software resume — all peripherals and SRAM reinitialise.
IWDG Reset
Independent watchdog running on LSI (~40 kHz). If not refreshed within timeout, triggers a reset. Wakes Standby as a reset event. LSI continues in all low-power modes.

## Slide 17
Practical Applications
STM32F103C8T6 Low-Power Design Scenarios
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
17 / 19
Source: DS5319 Rev. 20; RM0008 Rev. 21
Battery-Powered Sensor
MCU samples ADC periodically. Uses Stop mode between measurements. RTC alarm fires at sample interval; firmware restores HSE+PLL, reads sensor, stores data, returns to Stop.
Mode: Stop + RTC wake
Data Logger
Sleep mode keeps DMA and SPI active to buffer incoming data. CPU halted between DMA transfers. SysTick or DMA transfer-complete IRQ wakes CPU to process buffer.
Mode: Sleep + DMA IRQ
Industrial I/O Monitor
Stop mode during bus/sensor inactivity. GPIO EXTI line detects alarm or digital sensor edge. NVIC wakes CPU, firmware logs event, returns to Stop.
Mode: Stop + EXTI wake
CAN-Based Controller
Sleep mode when CAN bus is idle. bxCAN wake-up event on CAN activity (Sleep only — CAN does not wake from Stop). Deep Stop mode when entire node is inactive long-term.
Mode: Sleep + CAN IRQ
Portable Medical Device
Standby between patient measurement sessions. RTC alarm triggers measurement window. Full re-initialisation on wake; backup registers retain session state across Standby.
Mode: Standby + RTC wake
Wireless IoT Node
Stop mode between TX windows. RTC alarm wakes MCU, firmware prepares packet, activates RF, transmits, then returns to Stop. Minimise on-time to extend battery life.
Mode: Stop + RTC wake

## Slide 18
ATmega328P vs STM32F103C8T6 — Technical Comparison
Required 9-Row Comparison | DS5319 Rev. 20 | RM0008 Rev. 21 | ATmega328P Datasheet
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
18 / 19
Source: DS5319 Rev. 20; RM0008 Rev. 21; Atmel-7810 ATmega328P Datasheet
Feature | ATmega328P | STM32F103C8T6
Sleep modes | Idle, ADC Noise Reduction,Power-down, Power-save, Standby, Ext. Standby (6 modes) | Sleep, Stop, Standby (Shutdown: NOT supported on F103)
Deepest low-power mode | Power-down mode: All oscillators & clocks stopped; SRAM & registers retained; lowest static current state. | Standby mode: Voltage regulator disabled; 1.8V core powered down; SRAM & CPU registers lost.
Sleep-control registers | SMCR (SE, SM[2:0] — mode sel.); MCUCR (BODS, BODSE sleep ctrl); PRR (peripheral power-down) | SCB→SCR (SLEEPDEEP, SLEEPONEXIT); PWR_CR (PDDS, LPDS, DBP); PWR_CSR (EWUP, WUF, SBF)
Wake-up sources | INT0/INT1 (ext. interrupt pins), PCINT[23:0] (pin-change), Timer overflow, TWI addr, USART RX, ADC complete | EXTI lines 0–15 (GPIO), RTC alarm (EXTI 17), WKUP pin, NRST, IWDG reset, USB resume (Sleep/Stop)
External interrupt wake-up | INT0 on PD2, INT1 on PD3. Rising / falling / low-level. Configured via EICRA + EIMSK. Flag in EIFR. | EXTI lines 0–15 (any GPIO port). Rising / falling / both edges. AFIO_EXTICRx + EXTI_IMR/RTSR/FTSR. Flag in EXTI_PR; cleared by writing 1.
Timer operation during sleep | Idle: all timers run. Power-save: Timer2 async (32 kHz). Power-down: timers stopped. Standby: Timer2 async only. | Sleep: timers (TIM1–4) & SysTick run. Stop: all standard timers stopped. Standby: all standard timers stopped. (Only RTC in VBAT domain can run).
RTC operation | No dedicated RTC hardware. Timer2 can use ext. 32 kHz async. External RTC chip required for accurate calendar/alarm. | Built-in RTC in VBAT domain. Clocked by LSE (32.768 kHz). Operational in Stop + Standby. Alarm via EXTI line 17.
RAM retention | SRAM (2 KB) retained in all standard modes. EEPROM (1 KB) retained always. External Standby loses SRAM. | Sleep + Stop: 20 KB SRAM fully retained. Standby: SRAM lost. Backup registers (BKP) retained in all modes via VBAT domain.
Typical applications | Low-cost 8-bit embedded, Arduino-class systems, simple sensors, low-data-rate IoT, education | Professional 32-bit ARM systems, battery sensors, CAN/USB devices, motor control, industrial IoT, data loggers, medical devices

## Slide 19
Conclusion
STM32F103C8T6 Low-Power Architecture — Key Takeaways
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
19 / 19
Source: DS5319 Rev. 20; RM0008 Rev. 21
Architecture
STM32F103C8T6 is based on the 32-bit ARM Cortex-M3 (ARMv7-M) at up to 72 MHz with 64 KB Flash, 20 KB SRAM, and a rich peripheral set via AHB/APB1/APB2 buses.
Low-Power Operation
Three official modes: Sleep (CPU halted, clocks run), Stop (all clocks off, SRAM retained), Standby (1.8V domain off, SRAM lost). Correct register configuration of SCB, PWR, RCC, and EXTI is essential.
WFI and WFE
WFI (Wait For Interrupt) halts the CPU until a pending, enabled interrupt fires — ISR always executes. WFE (Wait For Event) halts until an event signal — ISR is optional. Both work with Sleep, Stop, and Standby modes.
Register Configuration
SCB→SCR.SLEEPDEEP selects Sleep vs Stop/Standby. PWR_CR.PDDS selects Stop vs Standby. PWR_CR.LPDS controls regulator in Stop. EXTI_IMR + NVIC_ISER enable wake-up sources. CWUF clears stale flags before sleep entry.
Important Restrictions
Shutdown mode: NOT supported by STM32F103C8T6 (newer STM32L/G families only). After Stop wake-up, clock defaults to HSI — firmware must restore HSE + PLL explicitly. After Standby, full re-initialisation required.

## Slide 20
THANK YOU!
STM32F103C8T6 | Low-Power Modes and Wake-Up Mechanisms
19 / 20